## Slide 1: event driven simulation using SystemC
编辑母版文本样式

## Slide 2: Introduction to SystemC
SystemC addresses system design and verification
  It focus on agile development of embedded SoC
  It’s designed to easily model complex circuit functionality
  But difficult to directly convert to RTL
Concept
Architecture
RTL
......
SystemC
High Level Modeling
RTL
Low Level Modeling

## Slide 3: Introduction to SystemC
SystemC contains a lot of high level features
  Embedded in C++, flexible and extensible
  Builtin event-driven simulation
  Support AMS for Analog/Mix-Signal modeling
  Support UVM for system verification

## Slide 4: This LAB
This lab is divided into 4 parts
  Basic SystemC: a simple adder module
  Event driven: a adder module with delay
  High level design: a pipelined multiplier
  High level design: a UART module

## Slide 5: Install depedency
Install systemc first
  apt install libsystemc-dev
Gtkwave is needed to show the waveform
  Please connect server using VNC

## Slide 6: Part 1. Basic SystemC
Basic SC Module
  SC_MODULE to define a module
  SC_CTOR to define construction method
  SC_METHOD to define functionality
  sensitive to define the sensitive list
When any var in the sensitive list changes, the function in SC_METHOD will be called immediately

## Slide 7: Part 1. Basic SystemC
Basic testbench
  sc_signal to define signal
  operator () to connect signal
  create trace vcd file and trace signal
  run random test
make run-01-adder

## Slide 8: Usage of GTKWave
Click “SST” to show signal list
Drag wire to “Signals” to show the signal
Ctrl + Scroll to scale time axis
Right click signal, you can change its format

## Slide 9: Part. 2. Event driven
SC thread wait event explicitly
  SC_THREAD to define a thread
  wait() to wait signal explicitly
The add function
  it is triggered when a or b changes
  then it delay 1ps and output a + b
  and wait next event

## Slide 10: Part. 2. Event driven
Delay is 4ps, signal changes every 2ps
  Use decimal format

## Slide 11: Part. 3. High level design
a pipelined multiplier
  latency = 3 cycle
  use std::deque to simulate the behavior
  sensitive to clk.pos()
code before the first wait() is reset logic
SC_THREAD active thread immediately
reset_signal_is define reset signal
  reset signal restart all thread
reset logic

## Slide 12: Part. 3. High level design
make run-03-mul

## Slide 13: Part. 4. High level design
UART: Universal Asynchronous Receiver/Transmitter
UART protocol: output 1 bit data in each cycle
  first output start bit ‘0’
  then 8 bit to represent the data
  finally 2 bits ‘11’ (usually 1.5bit, here is a simplified model)

## Slide 14: Part. 4. High level design
Try to use SC_THREAD to implement it
  before start, ready is 1
  when valid, set ready to 0, output start bit
  send each bit
  set stop bit, it takes 2 cycle
  ready is reset to 1 in the second stop bit

## Slide 15: Part. 4. High level design
make run-04-uart

## Slide 16: Part. 4. High level design
Imaging how to implement the module by Chisel
  Check how many states are there
    idle -> start -> send -> stop
  Check the state transition
  Implement each state
  Debug
It’s difficult to get it work in RTL
  In early development, high level model language is very important
  SystemVerilog is similar to SystemC
    but there is no opensource event-driven simulator