## Slide 1: FULL cycle simulation using verilator
编辑母版文本样式

## Slide 2: Introduction to Verilator
Verilator is the state-of-the-art RTL simulator
  support a lot of SystemVerilog feature
  compile Verilog / SystemVerilog to C++
Verilator Performance

## Slide 3: This LAB
This lab is divided into 4 parts
  use verilator to lint code
  write a simple C++ testbench
  use verilator to run coverage test
  build large design and tune compilation options

## Slide 4: Install depedency
apt install npm lcov cloc
npm install light-server

## Slide 5: Part. 1. Lint
In 01-simple, the ‘alu.sv’ has some typos
  check the output and fix the typos
verilator --lint-only alu.sv

## Slide 6: Part. 2. A Simple C++ Testbench
The testbench is a simple alu
  the detailed implementation is in alu.sv
  the functional equivalent module is in alu_tb.sv

## Slide 7: Part. 2. A Simple C++ Testbench
Add verilator compile command to Makefile
  --sv: this is a sv module
  --cc: compile to cpp
  --exe: build executable, not library
  --build: build after emit
  --trace: enable signal trace
  $^: means the alu.sv alu_tb.sv tb.cpp
    the order matters!

## Slide 8: Part. 2. Simple C++ Testbench
First tell verilator the command args
Instanciate the target module
Open trace file
Run test
Close trace file

## Slide 9: Part. 2. A Simple C++ Testbench
make, to ensure no compilation error
Then, we enumerate all funct, and generate test input
unlike SystemC, verilator has no timing information
  the time cycle is user managed tfp->dump(time++)

## Slide 10: Part. 2. A Simple C++ Testbench
make to compile and run
make show to show the waveform

## Slide 11: Part. 3. Coverage Test
In 02-coverage, the design is the same as 01
Modify the Makefile
  --coverage: turn on coverage test
  ./obj_dir/Valu: run target program to gen coverage data
  verilator_coverage: convert converage data

## Slide 12: Part. 3. Coverage Test
Add Code to export coverage data:
  run make to do coverage test

## Slide 13: Part. 3. Coverage Test
show coverage stat: make stat
There is only 97.1% coverage
lcov --summary cov.info
Reading tracefile cov.info
Summary coverage rate:
lines......: 97.1% (67 of 69 lines)
functions..: no data found
branches...: no data found

## Slide 14: Part. 3. Coverage Test
Open coverage report to find uncovered code
  ssh -L 4000:127.0.0.1:4000 root@115.27.161.184 -p xxxx
Open your browser, open http://localhost:4000
  modify the code to cover the

## Slide 15: Part. 3. Coverage Test

## Slide 16: Part. 4. Large Design
In 03-large, follow the README.md